## Slide 1: ACACES 2018 Summer School GPU Architectures: Basic to Advanced Concepts
Adwait Jog, Assistant Professor
College of William & Mary (http://adwaitjog.github.io/)
Slide Credits: NVIDIA Teaching Kit, Tor Aamodt (UBC)

## Slide 2: Course Outline
Lectures 1 and 2: Basics Concepts
  Basics of GPU Programming
  Basics of GPU Architecture
Lecture 3: GPU Performance Bottlenecks
  Memory Bottlenecks
  Compute Bottlenecks
  Possible Software and Hardware Solutions
Lecture 4: GPU Security Concerns
  Timing channels
  Possible Software and Hardware Solutions

## Slide 3: GPU Architecture Overview
Single-Instruction, Multiple-Threads
GPU
Interconnection Network
SM Cluster
SM
SM
Memory
Partition
GDDR5/HBM
Memory
Partition
GDDR5/HBM
Memory
Partition
GDDR5/HBM
Off-chip DRAM
SM Cluster
SM
SM
SM Cluster
SM
SM

## Slide 4: GPU Instruction Set Architecture (ISA)
NVIDIA defines a virtual ISA, called “PTX” (Parallel Thread eXecution)
More recently, Heterogeneous System Architecture (HSA) Foundation (AMD, ARM, Imagination, Mediatek, Samsung, Qualcomm, TI) defined the HSAIL virtual ISA.
PTX is Reduced Instruction Set Architecture (e.g., load/store architecture)
Virtual: infinite set of registers (much like a compiler intermediate representation)
PTX translated to hardware ISA by backend compiler (“ptxas”). Either at compile time (nvcc) or at runtime (GPU driver).

## Slide 5: Some Example PTX Syntax
Registers declared with a type:
.reg .pred p, q, r;
.reg .u16 r1, r2;
.reg .f64 f1, f2;
ALU operations
add.u32 x, y, z; // x = y + z
mad.lo.s32 d, a, b, c; // d = a*b + c
Memory operations:
ld.global.f32 f, [a];
ld.shared.u32 g, [b];
st.local.f64 [c], h
Compare and branch operations:
setp.eq.f32 p, y, 0; // is y equal to zero?
@p bra L1 // branch to L1 if y equal to zero

## Slide 6: GPU Microarchitecture
Companies tight lipped about details of GPU microarchitecture.
Several reasons:
  Competitive advantage
  Fear of being sued by “non-practicing entities”
  The people that know the details too busy building the next chip
Model described next, embodied in GPGPU-Sim, developed from: white papers, programming manuals, IEEE Micro articles, patents.

## Slide 7
GPGPU-Sim from UBC – A Cycle-level Simulator
Correlation
~0.976
12
Chart: HW - GPGPU-Sim Comparison

## Slide 8: Inside an SM
Fine-grained multithreading
  Interleave warp execution to hide latency
  Register values of all threads stays in core
SIMT
Front End
SIMD Datapath
Fetch
Decode
Schedule
Branch
Done (Warp ID)
Memory Subsystem
Icnt.
Network
SMem
L1 D$
Tex $
Const$
Reg
File

## Slide 9: Inside an SM (2.0)
Schedule
+ Fetch
Decode
Register
Read
Execute
Memory
Writeback
SIMT Front End
SIMD Datapath
ALU
ALU
ALU
I-Cache
Decode
I-Buffer
Score
Board
Issue
Operand
Collector
MEM
ALU
Fetch
SIMT-Stack
Done (WID)
Valid[1:N]
Branch Target PC
Pred.
Active
Mask
Three decoupled warp schedulers
Scoreboard
Large register file
Multiple SIMD functional units
Scheduler 1
Scheduler 2
Scheduler 3
Notes: As we learn more about the GPU design, we tried to add more detail to this model. At some point, we feel that we need to redesign from scratch.

## Slide 10: Fetch + Decode
Arbitrate the I-cache among warps
  Cache miss handled by fetching again later
Fetched instruction is decoded and then stored in the I-Buffer
  1 or more entries / warp
  Only warp with vacant entries are considered in fetch
Inst. W1
r
Inst. W2
Inst. W3
v
r
v
r
v
To
Fetch
Issue
Decode
Score-
Board
Issue
ARB
PC
1
PC
2
PC
3
A
R
B
Selection
T
o
I
-
C
a
c
h
e
Valid[1:N]
I-Cache
Decode
I-Buffer
Fetch
Valid[1:N]

## Slide 11: Instruction Issue
Select a warp and issue an instruction from its I-Buffer for execution
  Scheduling: Greedy-Then-Oldest (GTO)
  GT200/later Fermi/Kepler: Allow dual issue (superscalar)
  Fermi: Odd/Even scheduler
  To avoid stalling pipeline might
  keep instruction in I-buffer until
  know it can complete (replay)

## Slide 12: Scoreboard
Checks for RAW and WAW dependency hazard
  Flag instructions with hazards as not ready in I-Buffer (masking them out from the scheduler)
Instructions reserves registers at issue
Release them at writeback

## Slide 13: Review: In-order Scoreboard
Scoreboard: a bit-array, 1-bit for each register
  If the bit is not set: the register has valid data
  If the bit is set: the register has stale data
    i.e., some outstanding instruction is going to change it
Issue in-order: RD  Fn (RS, RT)
  If SB[RS] or SB[RT] is set  RAW, stall
  If SB[RD] is set  WAW, stall
  Else, dispatch to FU (Fn) and set SB[RD]
Complete out-of-order
  Update GPR[RD], clear SB[RD]
Regs[R1]
Regs[R2]
Regs[R3]
Regs[R31]
1
0
0
0
Register File
Scoreboard
[Gabriel Loh]
Notes: H&P-style notation

## Slide 14: In-Order Scoreboard for GPUs?
Problem 1: 32 warps, each with up to 128 (vector) registers per warp means scoreboard is 4096 bits.
Problem 2: Warps waiting in I-buffer needs to have dependency updated every cycle.
Solution?
  Flag instructions with hazards as not ready in I-Buffer so not considered by scheduler
  Track up to 6 registers per warp (out of 128)
  I-buffer 6-entry bitvector: 1b per register dependency
  Lookup source operands, set bitvector in I-buffer. As results written per warp, clear corresponding bit

## Slide 15: Example
- | - | - | -
- | - | - | -
Warp 0
Warp 1
ld r7, [r0]
mul r6, r2, r5
add r8, r6, r7
Index 0
Index 1
Scoreboard
Index 2
Warp 0
Warp 1
Instruction Buffer
i0 i1 i2 i3
Index 3
r7 | - | - | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
r7 | r6 | - | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 1 | 0 | 0
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 1 | 0 | 0
r7 | r6 | r8 | -
- | - | - | -
r7 | r6 | r8 | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 0 | 0 | 0
r7 | - | r8 | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 0 | 0 | 0
r7 | - | r8 | -
- | - | - | -
add r8, r6, r7 | 0 | 0 | 0 | 0
- | - | r8 | -
- | - | - | -
Code

## Slide 16: Operand Collector
(from instruction issue stage)
dispatch

## Slide 17: ALU Pipelines
SIMD Execution Unit
Fully Pipelined
Each pipe may execute a subset of instructions
Configurable bandwidth and latency (depending on the instruction)
Default: SP + SFU pipes

## Slide 18: Writeback
Each pipeline has a result bus for writeback
Exception:
  SP and SFU pipe shares a result bus
  Time slots on the shared bus is pre-allocated

## Slide 19: Memory Unit
Model timing for memory instructions
Support half-warp (16 threads)
  Double clock the unit
  Each cycle service half the warp
Has a private writeback path

## Slide 20: SM Cluster
Collection of SIMT cores

## Slide 21: GPU Architecture Overview
Single-Instruction, Multiple-Threads
GPU
Interconnection Network
SM Cluster
SM
SM
Memory
Partition
GDDR5/HBM
Memory
Partition
GDDR5/HBM
Memory
Partition
GDDR5/HBM
Off-chip DRAM
SM Cluster
SM
SM
SM Cluster
SM
SM

## Slide 22: Interconnection Network Model
Intersim (Booksim) a flit level simulator
  Topologies (Mesh, Torus, Butterfly, …)
  Routing (Dimension Order, Adaptive, etc. )
  Flow Control (Virtual Channels, Credits)
Two separate networks
  From SIMT cores to memory partitions
    Read Requests, Write Requests
  From memory partitions to SIMT cores
    Read Replies, Write Acks
Notes: 22

## Slide 23
Topology Examples
Notes: There are a diverse range of topologies that can be used to transfer memory requests in a many-core architecture.
In Nvidia’s GPUs, it looks something like a crossbar except multiple SIMT cores share input ports.
Intel’s Larrabee looks like a ring.
In our ISPASS paper we found that a mesh was viable as well.
23

## Slide 24: GPU Architecture Overview
Single-Instruction, Multiple-Threads
GPU
Interconnection Network
SM Cluster
SM
SM
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SM Cluster
SM
SM
SM Cluster
SM
SM

## Slide 25: Memory Partition
Interconnection Network
Memory Partition
L2
Cache
Bank
DRAM
Access
Scheduler
Off-Chip DRAM Channel
DRAM
Timing
Model
Atomic
Operation
Execution
ROP Queue
ICNTL2 Queue
L2DRAM Queue
DRAM Latency Queue
DRAML2 Queue
L2ICNT Queue

## Slide 26
DRAM
Column Decoder
Memory
Array
Row Decoder
Memory
Controller
Row Buffer
Row Buffer
Row Decoder
Column Decoder
Row Buffer
Column Decoder
Row Buffer
DRAM Access
Row access
  Activate a row or page of a DRAM bank
  Load it to row buffer
Column access
  Select and return a block of data in row buffer
Precharge
  Write back the opened row into DRAM
  Otherwise it will be lost!
Notes: Accessing data in DRAM consists of three steps: precharge, row access, and column access. A row access activates a page of data in the core and transfers it to the row buffer. After that, the column access selects the desired block and transfers it to the processor through the data bus.
26

## Slide 27: DRAM Row Access Locality
tRC = row cycle time
tRP = row precharge time
tRCD = row activate time
Notes: row access locality of a memory request stream is crucial to performance.
Within a bank, you have thousands of rows of data.
Before you can access a particular row, you have to load the row into the row buffer.
The time to close the previous row and open the new row is governed by the DRAM spec, and it can be a dominating factor in performance when there are few accesses per row, or low row access locality
27

## Slide 28
DRAM Bank-level Parallelism
To increase DRAM performance and utilization
  Multiple banks per DRAM chip
To increase bus width
  Multiple chips per Memory Controller
Notes: 28
You may have several chips connected in parallel to a controller to increase the bus width and the peak throughput.
Within a chip, you also have multiple banks to exploit bank-level parallelism. What this means is having multiple banks share the data bus to maximize utilization. If one bank is in the middle of switching rows, another bank can transfer data.
The BLP of memory request stream of an application is crucial to performance.
If you only use a single bank in a chip, any time it’s busy switching rows, that’s wasted data bus cycles.

## Slide 29
Scheduling DRAM Requests
Scheduling policies supported
    First in first out (FIFO)
      In-order scheduling
    First Ready First Come First Serve (FR-FCFS)
      Out of order scheduling
      Requires associative search

## Slide 30
Key GPU Performance Concerns

## Slide 31: Key GPU Performance Concerns
I) Data transfers between CPU and GPU are one of the major performance bottlenecks.
II) Data transfers between SMs and global memory is costly. Can on-chip memory help?
GPU Memory
Cache
ALU
Control
ALU
ALU
ALU
CPU Memory
Bottleneck!
GPU (Device)
Scratchpad
Registers and
Local Memory
GPU Global Memory
Bottleneck!
??
SM
SM
SM
SM
Notes: WARP_SIZE

## Slide 32: CUDA Streams
CUDA (and OpenCL) provide the capability to overlap computation on GPU with memory transfers using “Streams” (Command Queues)
A Stream orders a sequence of kernels and memory copy “operations”.
Operations in one stream can overlap with operations in a different stream.

## Slide 33: How Can Streams Help?
Serial:
Streams:
cudaMemcpy(H2D)
kernel<<<>>>
cudaMemcpy(D2H)
cudaMemcpy(H2D)
K0
DH0
K1
DH1
K2
DH2
Time
Savings
GPU idle
GPU idle
GPU busy

## Slide 34: CUDA Streams
cudaStream_t streams[3];
for(i=0; i<3; i++)
cudaStreamCreate(&streams[i]); // initialize streams
for(i=0; i<3; i++) {
cudaMemcpyAsync(pD+i*size,pH+i*size,size,
cudaMemcpyHostToDevice,stream[i]); // H2D
MyKernel<<<grid,block,0,stream[i]>>>(pD+i,size); // compute
cudaMemcpyAsync(pD+i*size,pH+i*size,size,
cudaMemcpyDeviceToHost,stream[i]); // D2H
}

## Slide 35: Manual CPU  GPU Data Movement
Problem #1: Programmer needs to identify data needed in a kernel and insert calls to move it to GPU
Problem #2: Pointer on CPU does not work on GPU since different address spaces
Problem #3: Bandwidth connecting CPU and GPU is order of magnitude smaller than GPU off-chip
Problem #4: Latency to transfer data from CPU to GPU is order of magnitude higher than GPU off-chip
Problem #5: Size of GPU DRAM memory much smaller than size of CPU main memory

## Slide 36: Additional Features in CUDA
Dynamic Parallelism (CUDA 5 onwards): Launch kernels from within a kernel. Reduce work for e.g., adaptive mesh refinement.
Unified Memory (CUDA 6 onwards): Avoid need for explicit memory copies between CPU and GPU
http://devblogs.nvidia.com/parallelforall/unified-memory-in-cuda-6/
See also, Gelado, et al. ASPLOS 2010.

## Slide 37: Key GPU Performance Concerns
I) Data transfers between CPU and GPU are one of the major performance bottlenecks.
II) Data transfers between SMs and global memory are costly. Can on-chip memory help?
GPU Memory
Cache
ALU
Control
ALU
ALU
ALU
CPU Memory
Bottleneck!
GPU (Device)
Scratchpad
Registers and
Local Memory
GPU Global Memory
Bottleneck!
??
SM
SM
SM
SM
Notes: WARP_SIZE

## Slide 38
Let’s consider some software approaches first..
before moving on to hardware approaches
Notes: WARP_SIZE

## Slide 39: GPU Memory Address Spaces
GPU has three address spaces to support increasing visibility of data between threads: local, shared, global
In addition two more (read-only) address spaces: Constant and texture.

## Slide 40: Partial Overview of CUDA Memories
Device code can:
  R/W per-thread registers
  R/W all-shared global memory
Host code can
  Transfer data to/from per grid global memory
Host
SM
GPU Global Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 41: CUDA Device Memory Management API functions
cudaMalloc()
  Allocates an object in the device global memory
  Two parameters
    Address of a pointer to the allocated object
    Size of allocated object in terms of bytes
cudaFree()
  Frees object from device global memory
  One parameter
    Pointer to freed object
Host
SM
GPU Global Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers

## Slide 42: Host-Device Data Transfer API functions
cudaMemcpy()
  memory data transfer
  Requires four parameters
    Pointer to destination
    Pointer to source
    Number of bytes copied
    Type/Direction of transfer
Host
SM
GPU Global Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers
Relatively new Features:
  Transfer to device can be asynchronous
Explicit mention of memcpy by the users can be avoided by new CUDA Unified Memory
https://devblogs.nvidia.com/unified-memory-cuda-beginners/

## Slide 43: Local address Space
Each thread has own “local memory”
0x42
Example: Location at address 100 for thread 0 is different from location at address 100 for thread 1.
Contains local variables private to a thread.

## Slide 44: Global Address Spaces
thread block X
thread block Y
Each thread in the different thread blocks (even from different kernels) can access a region called “global memory”.
Commonly in GPGPU workloads threads write their own portion of global memory. Avoids need for synchronization—slow; also unpredictable thread block scheduling.
0x42

## Slide 45: Blocks are partitioned after linearization
Linearized thread blocks are partitioned
  Thread indices within a warp are consecutive and increasing
  Warp 0 starts with Thread 0
Partitioning scheme is consistent across devices
  Thus you can use this knowledge in control flow
  However, the exact size of warps may change from generation to generation
DO NOT rely on any ordering within or between warps
  If there are any dependencies between threads, you must __syncthreads() to get correct results.

## Slide 46: Warps in Multi-dimensional Thread Blocks
The thread blocks are first linearized into 1D in row major order
  In x-dimension first, y-dimension next, and z-dimension last

## Slide 47: Example: Transpose (CUDA SDK)
__global__ void transposeNaive(float *odata, float* idata, int width, int height)
{
int xIndex = blockIdx.x * TILE_DIM + threadIdx.x; // TILE_DIM = 16
int yIndex = blockIdx.y * TILE_DIM + threadIdx.y;
int index_in = xIndex + width * yIndex;
int index_out = yIndex + height * xIndex;
for (int i=0; i<TILE_DIM; i+=BLOCK_ROWS) { // BLOCK_ROWS = 16
odata[index_out+i] = idata[index_in+i*width];
}
}
NOTE: “xIndex”, “yIndex”, “index_in”, “index_out”, and “i” are in local memory
(local variables are register allocated but stack lives in local memory)
“odata” and “idata” are pointers to global memory
(both allocated using calls to cudaMalloc -- not shown above)
1 | 2
3 | 4
1 | 3
2 | 4

## Slide 48: Scratchpad Memory
Each thread in the same thread block (work group) can access a memory region called scratchpad (or shared memory)
Shared memory address space is limited in size (16 to 48 KB).
Used as a software managed “cache” to avoid off-chip memory accesses.
Synchronize threads in a thread block using __syncthreads();
thread block
0x42

## Slide 49: Use of Scratchpad
__global__ void transposescratchpad (float *odata, float *idata, int width, int height)
{
__shared__ float tile[TILE_DIM][TILE_DIM];
int xIndex = blockIdx.x * TILE_DIM + threadIdx.x;
int yIndex = blockIdx.y * TILE_DIM + threadIdx.y;
int index_in = xIndex + (yIndex)*width;
xIndex = blockIdx.y * TILE_DIM + threadIdx.x;
yIndex = blockIdx.x * TILE_DIM + threadIdx.y;
int index_out = xIndex + (yIndex)*height;
for (int i=0; i<TILE_DIM; i+=BLOCK_ROWS) {
tile[threadIdx.y+i][threadIdx.x] = idata[index_in+i*width];
}
__syncthreads();
for (int i=0; i<TILE_DIM; i+=BLOCK_ROWS) {
odata[index_out+i*height] = tile[threadIdx.x][threadIdx.y+i];
}
}

## Slide 50: Bank Conflicts
To increase bandwidth common to organize memory into multiple banks.
Independent accesses to different banks can proceed in parallel
Bank 0
Bank 1
0 | 
2 | 
4 | 
6 | 
1 | 
3 | 
5 | 
7 | 
Example 1: Read 0, Read 1
(can proceed in parallel)
Example 2: Read 0, Read 3
(can proceed in parallel)
Bank 0
Bank 1
0 | 
2 | 
4 | 
6 | 
1 | 
3 | 
5 | 
7 | 
Example 3: Read 0, Read 2
(bank conflict)
Bank 0
Bank 1
0 | 
2 | 
4 | 
6 | 
1 | 
3 | 
5 | 
7 | 

## Slide 51: Shared Memory Bank Conflicts
__shared__ int A[BSIZE];
…
A[threadIdx.x] = … // no conflicts
0 | 
32 | 
64 | 
96 | 
1 | 
33 | 
65 | 
97 | 
31 | 
63 | 
95 | 
127 | 
2 | 
34 | 
66 | 
98 | 

## Slide 52: Shared Memory Bank Conflicts
__shared__ int A[BSIZE];
…
A[2*threadIdx.x] = // 2-way conflict
0 | 
32 | 
64 | 
96 | 
1 | 
33 | 
65 | 
97 | 
31 | 
63 | 
95 | 
127 | 
2 | 
34 | 
66 | 
98 | 

## Slide 53: Eliminate Bank Conflicts
__global__ void transposeNoBankConflicts (float *odata, float *idata, int width, int height)
{
__shared__ float tile[TILE_DIM][TILE_DIM+1];
int xIndex = blockIdx.x * TILE_DIM + threadIdx.x;
int yIndex = blockIdx.y * TILE_DIM + threadIdx.y;
int index_in = xIndex + (yIndex)*width;
xIndex = blockIdx.y * TILE_DIM + threadIdx.x;
yIndex = blockIdx.x * TILE_DIM + threadIdx.y;
int index_out = xIndex + (yIndex)*height;
for (int i=0; i<TILE_DIM; i+=BLOCK_ROWS) {
tile[threadIdx.y+i][threadIdx.x] = idata[index_in+i*width];
}
__syncthreads();
for (int i=0; i<TILE_DIM; i+=BLOCK_ROWS) {
odata[index_out+i*height] = tile[threadIdx.x][threadIdx.y+i];
}
}