## Slide 1: Breaking the Memory Wall in Current and Emerging Accelerators
Adwait Jog
Assistant Professor
College of William & Mary
http://adwaitjog.github.io/

## Slide 2: Research Group
  Architecting general-purpose and domain-specific accelerators for superior
    Performance/Throughput
    Reliability and Security
    Energy Efficiency
    Fairness
More details: http://insight-archlab.github.io/

## Slide 3: Why Accelerators?
Parallelism
Large
Data Sets
Large Number of Compute Elements
Optimized for Throughput
Great for
Parallel Code
Accelerator
High Speed
Better Energy Efficiency

## Slide 4: How Acceleration Works
Fewer Cores
Optimized for Latency
Great for Sequential Code
Large Number of Compute Elements
Optimized for Throughput
Great for
Parallel Code
Accelerator
Communication
Notes: Do not use the word “offload”

## Slide 5: Memory Wall and Accelerators
General purpose (e.g., GPU)
  Latency: Multi-threading
  Capacity: Virtualization and UVM
  Bandwidth: Memory to Compute Movement of Data
    Hurts throughput / energy efficiency, exposes new attack vectors
Domain-specific
  Latency/Bandwidth: Non-von Neumann architectures; spatial architectures; in-memory architectures
  Capacity: Limited to no support for virtualization
    Hurts throughput and reduces applicability

## Slide 6: Architectural Support for Efficient Large-Scale Automata Processing
Joint work with
Hongyuan Liu, Mohamed Ibrahim (College of William & Mary),
Onur Kayiran (AMD), Sreepathi Pai (University of Rochester),
Appeared at MICRO 2018
Notes: Hi, my name is Hongyuan Liu. Today, I will present our work “Architectural Support for Efficient Large-Scale Automata Processing”.
This work was jointly performed with my advisor and colleagues
at The College of William and Mary
and
our collaborators at AMD and University of Rochester.

## Slide 7: Finite State Machine (Automata) Processing
Widely used in several areas
Existing general-purpose architectures (CPUs and GPUs) are not efficient at FSM processing
  Irregular memory accesses
  Limited Parallelism
Notes: Finite state machines are widely used in different areas such as Bioinformatics, machine learning, networking intrusion detection, and XML parsing.
However, traditional von Neumann architectures are not efficient at FSM processing because of irregular memory accesses, and limited parallelism.

## Slide 8: Automata Processor (AP)
Figure from Micron website
In-memory Processing
Parallelism
  FSMs
  States
Notes: Automata Processor AP is a DRAM based domain specific architecture for accelerating finite state machine processing.
The automata processor performs orders of magnitude better than CPUs.
Generally, there are two reasons.
First, it exploit in-memory processing. This does not require expensive data movement.
Second, it has high amount of parallelism --- Multiple FSMs can run simultaneously, and multiple states can be activated simultaneously.

## Slide 9: Background on FSM processing and its execution on AP

## Slide 10
FSM
  APPLE
  APPLICATION
Input Stream
  APPLEC
Starting State
(Always-enabled)
Starting state
State
Reporting state
A
Match-set
Enabled State
Activated State
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
Notes: First, we show some backgrounds on the FSM processing.
Here is an FSM. It can identify two patterns, which are APPLE, and APPLICATION.
An FSM-based application contains multiple FSMs.
The matching process starts from the starting state, which is always enabled during the execution in our context.
The FSM-based application also requires an input stream. Here we show it as “APPLEC”.
We will show the example matching process in the following a few slides.

## Slide 11
APPLEC
Active
Starting state
State
Reporting state
A
Match-set
Enabled State
Activated State
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
Notes: Here we show the matching process.
In this example,
the first symbol is A. This activates the starting state S0.

## Slide 12
APPLEC
Starting state
State
Reporting state
A
Match-set
Enabled State
Activated State
Enabled
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
Notes: When S0 is activated, it enables its successor S1.

## Slide 13
APPLEC
Starting state
State
Reporting state
A
Match-set
Enabled State
Activated State
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
Notes: The second symbol is P. This activates S1.

## Slide 14
APPLEC
Starting state
State
Reporting state
A
Match-set
Enabled State
Activated State
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
Notes: The activated S1 enables its successor S2.

## Slide 15
APPLEC
Report generated
Starting state
State
Reporting state
A
Match-set
Enabled State
Activated State
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
Notes: This process continues. After several cycles, when E comes, reporting state S4 is activated.
A report is generated in this case.

## Slide 16
APPLEC
Starting state
State
Reporting state
A
Match-set
Enabled State
Activated State
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
Notes: The matching process continues until all symbols in the input stream are consumed.

## Slide 17: FSM Processing on AP

## Slide 18
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
  Input Stream: APPLEC

## Slide 19
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 20
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
‘A’
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 21
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
‘A’
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 22
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 | 1 |  |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 23
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 | 1 |  |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
‘P’
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 24
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  | 1 |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 25
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  | 1 |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
‘P’
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 26
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  |  | 1 |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 27
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  |  | 1 |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
‘L’
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 28
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  |  |  | 1 | 1 |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 29
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  |  |  | 1 | 1 |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
‘E’
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 30
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 31
S0 | S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11
1 |  |  |  |  |  |  | 1 |  |  |  | 
 |  |  |  |  |  | 1 |  |  |  |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 
 |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  | 1 |  |  |  |  |  |  |  | 
 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  |  | 
Input Symbol
8x256 Decoder
‘A’
‘C’
‘E’
‘L’
‘P’
‘B’
‘D’
State Bit
…
…
Routing Matrix
  Input Stream: APPLEC
‘C’
P
P
L
E
A
I
C
A
T
I
O
N
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11

## Slide 32: Problem

## Slide 33: Applications are getting larger
ClamAV: Anti-virus database that identifies virus characteristics via FSMs
Snort: Network intrusion detection identifies many intrusion patterns via FSMs
Many more…
Notes: However, there is sill a problem when we use AP to do the FSM processing.
For example, currently,
there are many emerging applications that consist of many FSM states.
For example, ClamAV is an anti-virus application. Each characterization of virus is stored as an FSM. Therefore, the database of virus is increasing over time.
Another example is Snort, where it uses FSM to represent each intrusion pattern.
We expect such applications will become more common in the future.

## Slide 34
Applications are getting larger
AP Capacity is Limited
How do we accelerate large-scale FSM processing?
Notes: As a result, there is a challenge to use AP efficiently.
On one side, the applications are getting larger.
On the other side, the AP capacity is limited.
In this research, we focus on how to accelerate large-scale FSM processing using automata processor.

## Slide 35: Current situation: Repeated Executions
Application
Input Stream:
ORANGEAPPLEBANANAPEARPEACH….
Configure Batch 1
1st Execution
Notes: An application consists of many FSMs.
If the number of FSM states cannot fit in AP at one time, multiple batches are needed.
For example, we configure the first batch to the AP, and run the input stream on it.

## Slide 36: Current situation: Repeated Executions
Application
Input Stream:
ORANGEAPPLEBANANAPEARPEACH….
2nd Execution
Configure Batch 2
Notes: Then, we configure the second batch to the AP, and run the same input stream on it AGAIN.
This execution repeats until all batches are configured and executed on AP.
This repeated executions lead to inefficiencies.

## Slide 37: Observation and Motivation

## Slide 38
After the execution
  Some states are never enabled (cold)!
P
P
L
E
A
I
C
A
T
I
O
N
Cold States
Hot States
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
Notes: To revisit the example we show before, we found there might be a number of states are configured to AP, but are never used.
We call them cold states in our work, while the enabled states are hot states in our work.
We found that, in the previous example, S6 to S11 are cold.

## Slide 39: Underutilization of AP
Because of mismatch, there are many cold states configured to AP.
Chart: Percentage of States
| CAV4k | DS | CAV | DS03 | DS06 | Snort_L | DS09 | Snort | HM1500 | HM500 | HM1000 | HM | PEN | TCP | Rg1 | EM | ER | Rg05 | Fermi | Pro | Brill | LV | Bro217 | SPM | RF1 | RF2
Hot (Enabled) | 0.0097925 | 0.090483 | 0.09952 | 0.10861 | 0.11772 | 0.11825 | 0.12396 | 0.16185 | 0.1749 | 0.17492 | 0.17552 | 0.25815 | 0.353 | 0.3751 | 0.45483 | 0.46338 | 0.47128 | 0.47437 | 0.55766 | 0.70392 | 0.73325 | 0.78772 | 0.89965 | 0.91361 | 0.94863 | 0.97288
Cold (Never-enabled) | 0.99021 | 0.90952 | 0.90048 | 0.89139 | 0.88228 | 0.88175 | 0.87604 | 0.83815 | 0.8251 | 0.82508 | 0.82448 | 0.74185 | 0.647 | 0.6249 | 0.54517 | 0.53662 | 0.52872 | 0.52563 | 0.44234 | 0.29608 | 0.26675 | 0.21228 | 0.10035 | 0.086388 | 0.051367 | 0.027122
Notes: Going forward, we evaluate all these real applications.
In this figure, the y-axis is the percentage of states.
We found that a large portion of states are cold. On average, there are 59% of cold states.
The reason of cold states is mismatch, where there are not enough interesting patterns occur in the input stream.

## Slide 40: Benefits of only configuring hot states
Time
Notes: So, ideally, if we can only configure the hot states, we can get performance benefits.
Here is an example illustrating the performance benefits of configuring only hot states.
In the baseline case,
the application is split to two batches.
At runtime, the AP needs to execute the same input stream for each batch.
On the contrary,
now suppose we have an oracular knowledge of cold states,
and in this case, the hot states could fit in one batch.
In comparison, at runtime, the AP only executes the input stream once, which leads to significant cycle savings.

## Slide 41: Outline
Introduction
Background and Motivation
Challenges and Our Approach
Results
Conclusions
Notes: Next, to realize the benefits as much as possible, we will discuss the challenges and our approach.

## Slide 42: Challenges
How do we predict and partition?
How do we handle the mispredictions?
Notes: However, to realize the benefits, we have two challenges.
First, how do we predict a state is cold or hot at compile time?
Second, how do we partition the FSMs in the application, and only configure the hot states?

## Slide 43: Which states are more likely to be hot?
P
P
L
E
A
I
C
A
T
I
O
N
Chart: Percentage of Hot States
| CAV4k | DS | CAV | DS03 | DS06 | Snort_L | DS09 | Snort | HM1500 | HM500 | HM1000 | HM | PEN | TCP | Rg1 | EM | ER | Rg05 | Fermi | Pro | Brill | LV | Bro217 | SPM | RF1 | RF2
Shallow | 0.0096138 | 0.087932 | 0.076487 | 0.10367 | 0.10665 | 0.087901 | 0.11077 | 0.12851 | 0.16583 | 0.16589 | 0.16616 | 0.19813 | 0.20798 | 0.22533 | 0.2569 | 0.19858 | 0.25316 | 0.25695 | 0.16262 | 0.2683 | 0.27784 | 0.18103 | 0.2487 | 0.3 | 0 | 0
Medium | 0.00010934 | 0.0023227 | 0.018753 | 0.0046937 | 0.0085443 | 0.018317 | 0.0087684 | 0.023845 | 0.009071 | 0.0090328 | 0.0093648 | 0.056848 | 0.10253 | 0.087698 | 0.13904 | 0.12868 | 0.15194 | 0.16092 | 0.15475 | 0.25306 | 0.24417 | 0.38578 | 0.26254 | 0.34893 | 0.05 | 0.05
Deep | 6.9337e-05 | 0.00022813 | 0.0042795 | 0.00024704 | 0.0025316 | 0.01203 | 0.0044244 | 0.0094888 | 0 | 0 | 0 | 0.0031729 | 0.04248 | 0.062069 | 0.05889 | 0.14403 | 0.058284 | 0.056493 | 0.2403 | 0.18256 | 0.21124 | 0.22091 | 0.38841 | 0.26469 | 0.89863 | 0.92288
Shallow states  Hot.
Deep states  Cold (Details in the paper)
Notes: First, we study which states are more likely to be hot.
Consider the previous example, we found the shallow states are hot.
This is because, the matching process is always from lower topological order to higher topological order.
---- We define a state is shallow or deep based on its topological order.
We study the hot states in these applications. We found that the shallow states are more likely to be hot.
Similarly, deep states are more likely to be cold.

## Slide 44: How do we partition?
AP
P
P
L
E
A
I
C
A
T
I
O
N
We use a simple but effective offline profiling mechanism to determine the partition topological-order. (More details in the paper)
Partition via topological order makes transition unidirectional.
Topological Order
K = 5
Notes: Based on this observation, we propose to use topological order to partition the FSMs.
Consider the previous example, we can partition it at topological order K = 5.
We only configure the states with topological orders no greater than 5 to the AP.
-----------------------------------------------
To determine the partitioning topological order for each FSM in the application, we use a simple offline profiling mechanism.
Second, partition via topological order makes transition unidirectional. Therefore, no back and forth transition will happen, which simplifies the misprediction handling. We will show it later.

## Slide 45: How do we handle the mispredictions?
AP
APPLICATION
S3; cycle 3
Generated intermediate report
P
P
L
E
A
I
C
A
T
I
O
N
S3
S4
S5
S2
K = 3
Intermediate
reporting state
P
P
A
L
S3’
S2
AP
P
P
A
L
S2
S3’
Notes: However, it is hard to predict the topological order correctly.
Now, suppose we have an imperfect partition at topological order k = 3.
In this partition,
--- S3, S4, S5 were partitioned out of AP, but they are actually hot. ----
In this case, a transition may go outside of the AP.
To notify the handler about the mispredictions, we add an intermediate reporting state for each cutting edge across the partition topological order.
In this case, the cutting edge is S2 to S3.
Then we attach S3’ to S2.
Therefore, in addition to the predicted hot states, the intermediate reporting states are also configured to AP.
-----------------------------------------------------
Consider current input steam is APPLICATION instead. The current symbol is L.
It makes the intermediate reporting state S3’ activated. So, an intermediate report is generated.
The report consists of two parts.
First, the state that to be continued in the misprediction handling.
Second, the cycle number where the report was generated.
In the following slides, we will show how to handle the list of generated intermediate reports.

## Slide 46: Handle the mispredictions --- SparseAP
Time
Cycle 5
Cycle 14
Notes: To handle the intermediate reports caused by mispredictions, we propose SparseAP, which is an execution mode of AP.
It has two operations.
First, the enable operation enables the state to be continued in the matching process.
Second, the jump operation that jumps to a certain input position.
====
Here, we consider the realistic partition case. We partition the FSM states to predicted hot set, and predicted cold set.
We configure the predicted hot set to the BaseAP. During the BaseAP execution, transitions coming out the scope of predicted hot set are recorded in a list of intermediate reports.
In this example, the AP execution generates two intermediate reports, which are shown in (a) and (b).
After the AP execution, we handle the generated intermediate reports using SparseAP mode. We configure the predicted cold states to the SparseAP mode.

## Slide 47: Handle the mispredictions --- SparseAP
Time
Notes: Suppose the intermediate reports were generated at cycle 5 and cycle 14.

## Slide 48: Handle the mispredictions --- SparseAP
Time
Notes: At SparseAP mode, since there is no enabled state initially, we perform a jump operation to cycle 5 directly.
We enable the state that is to be continued.
After several cycles, there is no state enabled in SparseAP. This is either because of mismatch, or because a report is generated.

## Slide 49: Handle the mispredictions --- SparseAP
Time
Notes: Then the SparseAP performs a jump operation again. This jumps to the cycle where the second intermediate report was generated, which is 14.

## Slide 50: Handle the mispredictions --- SparseAP
Time
Notes: After several cycles, there is no enabled state, and there is no intermediate reports to be handled. This finishes the SparseAP execution.

## Slide 51: Evaluation Methodology
Our baseline AP
  AP half-core
We build our evaluations on VASim
Benchmarks
  ANMLZoo
  RegEx
Offline profiling and testing input
  0.1% and 1% of input as representative profiling input.
  The rest is the testing input.
Notes: We use an AP half-core as our baseline architecture.
We build our evaluations on VASim, which is a cycle-accurate simulator for automata processing.
We use two entire benchmark suites, ANMLZoo and Regex.
We use 0.1% and 1% of 1MB input as our representative input in the compiling time. We use the rest of input as our testing input.

## Slide 52: Speedup
Speedup is related to the underutilization of each application
  Limited improvement when NFAs have SCC or when applications are small
Chart: Speedup
| CAV4k | HM1500 | HM1000 | Snort_L | HM500 | SPM | DS | ER | RF1 | Snort | CAV | Brill | Pro | Fermi | PEN | RF2 | GeoMean
0.1% | 47 | 2.9243 | 2.6913 | 3.1938 | 2.1209 | 0.80988 | 3.9998 | 0.82021 | 1 | 1.4837 | 2.9901 | 1.0803 | 1.214 | 1 | 0.22873 | 1 | 1.7649
1% | 47 | 3.6733 | 3.2722 | 5.0419 | 2.4645 | 1.0042 | 4 | 1 | 1 | 2.9993 | 2.9901 | 1.6516 | 1.6077 | 1 | 0.30555 | 1 | 2.1479
47x
1.8
2.1
Notes: Over the evaluated applications, our approach achieves up to 47x speedup.
Our approach achieves 1.8x and 2.1x speedup respectively on average using 0.1% and 1% profiling input.
The speedup is also related to the underutilization of each application.

## Slide 53: Performance per area
Chart: Performance per STE (*10000)
| CAV4k | HM1500 | HM1000 | Snort_L | HM500 | SPM | DS | ER | RF1 | Snort | CAV | Brill | Pro | Fermi | PEN | RF2 | TCP | DS06 | Rg05 | Rg1 | EM | DS09 | DS03 | HM | LV | Bro217 | Avg
Baseline | 0.0086575 | 0.027127 | 0.04069 | 0.067817 | 0.08138 | 0.08138 | 0.10173 | 0.10173 | 0.10173 | 0.13563 | 0.13563 | 0.20345 | 0.20345 | 0.20345 | 0.20345 | 0.20345 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.22961
AP/SpAP | 0.4069 | 0.099646 | 0.13315 | 0.34192 | 0.20056 | 0.081724 | 0.4069 | 0.10173 | 0.10173 | 0.4068 | 0.40556 | 0.33601 | 0.32708 | 0.20345 | 0.062164 | 0.20345 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.4069 | 0.30338
32% improvement in performance per area
More results are in the paper
  Resource savings
  Sensitivity to AP capacity
  Effectiveness of SparseAP
  …
32.1%
Notes: To measure the utilization efficiency of AP, we use a metric --- performance per area.
From this result, our approach achieves 32.1% improvement in terms of performance per STE.
More results are in the paper.

## Slide 54: Conclusions
We show that many FSM states are cold (never-enabled) on AP leading to its underutilization.
We propose a novel topological-order based partitioning mechanism for FSMs that partitions only predicted hot states on AP.
We handle the mispredictions using a new execution mode (SparseAP) of AP.
Our low-overhead hardware/software approach achieves 2.1× geometric mean speedup (up to 47×) across 26 applications.

## Slide 55: Memory Wall and Accelerators
General purpose (e.g., GPU)
  Latency: Multi-threading
  Capacity: Virtualization, UVM, Multi-app Support
  Bandwidth: Memory to Compute Movement of Data
    Hurts throughput / energy efficiency, exposes new attack vectors
Domain-specific
  Latency/Bandwidth: Non-von Neumann architectures; spatial architectures, in-memory architectures
  Capacity: Limited to no support for virtualization
    Hurts throughput and reduces applicability

## Slide 56: Memory Bandwidth Wall
Sub-optimal throughput
Chart: 
| SAD | PVC | SSC | BFS | MUM | CFD | KMN | SCP | FWT | IIX | SPMV | JPEG | BFSR | SC | FFT | SD2 | WP | PVR | BP | CON | AES | SD1 | BLK | HS | SLA | DN | LPS | NN | PFN | LYTE | LUD | MM | STO | CP | NQU | CUTP | HW | TPAF | AVG | AVG-T1
 | 0.90269 | 0.86445 | 0.82241 | 0.6484 | 0.71382 | 0.60663 | 0.60584 | 0.43943 | 0.47385 | 0.64708 | 0.64635 | 0.51687 | 0.46336 | 0.4493 | 0.29411 | 0.28971 | 0.47774 | 0.26293 | 0.24463 | 0.16514 | 0.18735 | 0.13915 | 0.15322 | 0.094841 | 0.11532 | 0.1988 | 0.10324 | 0.10689 | 0.048452 | 0.13028 | 0.088976 | 0.041891 | 0.012271 | 0.011149 | 0.00013977 | 0.0053883 | 0.0050535 | 0.0021302 | 0.31524 | 0.54577
55%
GPGPU Applications
Percentage of total execution cycles wasted waiting for the data

## Slide 57: Memory Coalescing
Reduces Redundant Thread Requests in a deterministic manner
  Popular way to reduce memory traffic
However it can expose an attack vector
Can we thwart in a low-overhead manner?

## Slide 58: RCoal: Mitigating GPU Timing Attack via Subwarp-based Randomized Coalescing Techniques
Appeared at HPCA 2018
Joint Work with
Gurunath Kadam (College of William and Mary)
Danfeng Zhang (Penn State University)
Notes: Hi, my name is Hongyuan Liu. Today, I will present our work “Architectural Support for Efficient Large-Scale Automata Processing”.
This work was jointly performed with my advisor and colleagues
at The College of William and Mary
and
our collaborators at AMD and University of Rochester.

## Slide 59: Memory Access Coalescing in GPUs
Streaming Multiprocessor
Warp pool
Warp
Thread # 1
Thread # 32
. . .
Warp Scheduler
LD/ST Unit
Global Memory
Coalescing Unit

## Slide 60: Memory Access Coalescing in GPUs
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x00
0x04
0x07
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
WARP
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 1
Block Address # 2

## Slide 61: Memory Access Coalescing in GPUs
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
0x00
0x04
0x07
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
WARP
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 2

## Slide 62: Security Concerns
GPUs may be accelerating cryptographic applications (e.g., AES, RSA etc.) and authentication algorithms on-behalf of CPUs (Graviton, OSDI’18)
GPUs may be accelerating applications that are using user-sensitive data (e.g., genomics, financial)
It is imperative to keep GPUs secure against a variety of side-channel attacks and other security vulnerabilities.

## Slide 63: Security Attacks
User’s web activity on GPU can be tracked by the malicious attacker who is co-located on the same card [Oakland 2014]
AES private keys can be recovered by correlation timing attacks [HPCA 2016]
More severe attacks on GPUs? [Oakland’18]
  Spectre/Meltdown like attacks for GPUs?

## Slide 64: Correlation Timing Attacks
Plaintexts | Ciphertexts | Time duration
Plaintext # 1
time1
timestart
- timestop = time1
Plaintext # 2
time2
Plaintext # 3
time3
…
…
Attacker
Server
Ciphertext # 1
Ciphertext # 2
Ciphertext # 3
…
K1 , K2 , … ,
Ki
, …
Key guesses
Correct Key
Correct Key??
Notes: This should be a general timing attack description

## Slide 65: Correlation Timing Attack
Execution time < -- > coalesced accesses
  GPU memory leakage
Private keys / cipher text < -- > coalesced accesses
  GPU compute leakage

## Slide 66: Coalesced Accesses and Execution Time
Associate the number of coalesced accesses with execution time
Notes: Say on our set-up

## Slide 67: Last Round of AES on GPU

## Slide 68: Last Round of AES on GPU
LINE # 1
LINE # 2
LINE # 32
…
…
ti1
ti2
ti32
.
.
.
Input text
to Last Round
…
…
.
.
.
Thread # 1
Thread # 2
.
.
.
Thread # 32
.
.
.
T4[ti2]
T4[ti1]
T4[ti32]
Request # 1
Request # 2
.
.
.
Request # 32
Coalescing
Unit
.
.
.
⊕ kj
⊕ kj
⊕ kj
Replies # 1
Replies # 2
.
.
.
Replies # 32
cj1
cj2
cj32
.
.
.
Ciphertext

## Slide 69: Correlation Timing Attack on GPU
Goal of the attack: Recover the AES Key (byte-by-byte)
Last Round of AES is vulnerable
Last Round is invertible
Memory access
of thread tid
How an attacker can calculate the number of coalesced accesses?
Notes: After the goal, Attack model – using figure slide 2. What is available to the attacker – ciphertext, execution time and AES Tables.

## Slide 70: Attacker calculates the # of coalesced accesses
…
…
cj1
cj2
cj32
.
.
.
Ciphertext
.
.
.
⊕ kjm
⊕ kjm
⊕ kjm
.
.
.
.
.
.
T4-1[cj2⊕kjm]
T4-1[cj1⊕kjm]
T4-1[cj32⊕kjm]
ti1,m
ti2,m
ti32,m
.
.
.
Guessed Table
Lookup Indices
.
.
.
.
.
.
Coalesced Accesses
(Ajm,n)
Correct value of key byte?

## Slide 71: Finding the Correct Key Value
Attacker encrypts ‘N’ number of plaintexts over server
  Records Ciphertext and Execution time
Aj0,1, Aj0,2, . . . . , Aj0,N
E1,E2,...,EN
Key Guess 0
Key Guess 1
Key
Guess 255
Corrj0
Corrj1
Corrj255
Key
Guess α
Corrjα
Maximum Correlation
Aj1,1, Aj1,2, . . . . , Aj1,N
Ajα,1, Ajα,2, . . . . , Ajα,N
Aj255,1, Aj255,2, . . . . ,Aj255,N
.
.
.
.
.
.
.
.
.
.
.
.
Recorded
Execution Time
Correct
Key Byte
# of Coalesced Accesses
Correlations
Notes: Eliminate the slide transition

## Slide 72: Simulating Timing Attack on our Set-up
Correct guess
Incorrect guesses
Why is Correlation Timing Attack possible?
The baseline attack leverages the deterministic nature of the coalescing mechanism
AES key value affects the coalesced accesses
# coalesced accesses affects the execution time
How to mitigate Correlation Timing Attacks on GPU?
Answer: By making it harder for the attacker to correctly calculate the number of coalesced accesses
Notes: TODO: Coalescing good for performance and bad for security

## Slide 73: Naïve Solution
Disable coalescing altogether?
  Correlation drops to ~0
  Correct key byte is indistinguishable
Up to 178% performance degradation
  Degradation increases with plaintext size
Correct guess
Naïve solution is Good for Security, Bad for Performance
Offers no tradeoff
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 74: RCoal: Fixed Sized Subwarp (FSS)
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
DEFAULT: number of subwarps = 1
0x00
sid = 0
0x04
0x07
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
FSS: number of subwarps = 2
0x00
sid = 0
0x04
0x07
sid = 1
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Notes: Fixed Size Subwarp eliminates the fixed number of subwarps based determinism.

## Slide 75: FSS Security against Baseline Attack
Correlation between the number of coalesced accesses and the execution time drops
Correct key byte is harder to find
Improved security

## Slide 76: FSS Performance
Memory accesses increase with number of subwarps
Execution time increases with number of subwarps
Performance degrades as number of subwarp increase
Can attacker still recover the AES key?
Notes: Better transition going into FSS attack

## Slide 77: FSS against FSS attack
Attacker can figure out the number of subwarps
Notes: Why FSS attack?

## Slide 78: FSS against FSS attack
Attacker can figure out the number of subwarps
Attacker can calculate per subwarp accesses
Correct guess

## Slide 79: FSS against FSS attack
Attack possible when the attacker can figure out number of subwarps!
  Coalescing still deterministic
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 80: RCoal: Random Sized Subwarp (RSS)
Size distribution
Normal Distribution
Skewed Distribution
Mean of the distribution is same as FSS
Security and performance similar to FSS
We select RSS with Skewed Distribution
Mean of the distribution is different than FSS
Large subwarp offers better coalescing
Improved security compared to FSS
Improved performance compared to FSS


RCoal to mitigate the correlation timing
attacks
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 81: RCoal: Random-Threaded Subwarp (RTS)
FSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 0
0x06
sid = 1
0x07
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
FSS+RTS: number of subwarps = 2
0x00
0x01
0x06
0x07
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x04
0x05
0x06
0x07
sid = 0
sid = 0
sid = 1
sid = 1

## Slide 82: RCoal: Random-Threaded Subwarp (RTS)
RSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 1
0x06
0x08
tid = 0
tid = 1
tid = 2
tid = 3
RSS+RTS: number of subwarps = 2
0x00
sid = 1
0x01
0x06
sid = 0
0x08
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B

## Slide 83: Evaluation Set-up
AES-128
Plaintext with 32 lines
GPGPU-SIM
  15 SMs, 32 threads/warp, one subwarp per coalescing unit (base case)
  GDDR5 Memory with 6 MCs, 16 DRAM-banks, 4 bank-groups/MC
Enhanced Attack Algorithms
  Corresponding Attacks

## Slide 84
Chart: Number of Subwarp
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0
FSS | 0.99846 | 0.99941 | 0.99935 | 0.99771 | 0.94154 | 0
FSS+RTP | 0.99846 | 0.42426 | 0.2569 | 0.080777 | 0.04366 | 0
RSS | 0.99846 | 0.2467 | 0.15489 | 0.13513 | 0.14823 | 0
RSS+RTP | 0.99846 | 0.15216 | 0.095578 | 0.10696 | 0.065268 | 0
Chart: Number of Subwarps
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0
FSS | 1 | 1.0822 | 1.1525 | 1.2189 | 1.2788 | 1.3801
FSS+RTS | 1 | 1.082 | 1.1527 | 1.2198 | 1.2787 | 1.3801
RSS | 1 | 1.0538 | 1.104 | 1.1534 | 1.2455 | 1.3801
RSS+RTS | 1 | 1.0544 | 1.1013 | 1.1547 | 1.2455 | 1.38
Security
(Lower the better)
Execution Time
(Lower the better)
Offers Security/Performance Trade-off
Notes: Mention Rcoal in a BOX

## Slide 85: Conclusions
We proposed RCoal, a set of three novel defense mechanisms
  To mitigate the correlation timing attacks
  Randomizes the memory access coalescing
  Scales with the plaintext size (analysis in paper)
  Theoretical analysis in the paper
RCoal offers a trade-off between security and performance and improves security at a modest performance loss.
Notes: Try to reduce background and introduce rcoal_score

## Slide 86: Acknowledgements
More details: http://insight-archlab.github.io/
Gurunath Kadam
(Ph.D. student)
Mohamed Ibrahim (Ph.D. Student)
Fan Luo
(MS student, graduated)
Hongyuan Liu
(Ph.D. student)
Haonan Wang
(Ph.D. student)
Adwait Jog
(PI)
Thank you!
Questions?
(Email: ajog@wm.edu)

## Slide 87: Backup Slides

## Slide 88: Jump Ratio

## Slide 89: Sensitivity results: capacity = 49K
Chart: Speedup
| CAV4k | HM1500 | HM1000 | Snort_L | HM500 | SPM | DS | ER | RF1 | Snort | CAV | GeoMean
0.1% | 24 | 1.6 | 1.8421 | 2.9752 | 1.5 | 0.95673 | 2 | 0.45982 | 1 | 2 | 2 | 1.8918
1% | 24 | 1.6 | 2.4319 | 2.9761 | 1.5 | 1.0034 | 2 | 1 | 1 | 2 | 2 | 2.0913
24x
1.9x
2.1x

## Slide 90: Sensitivity results: capacity = 12K
Chart: Speedup
| CAV4k | HM1500 | HM1000 | Snort_L | HM500 | SPM | DS | ER | RF1 | Snort | CAV | Brill | Pro | Fermi | PEN | RF2 | TCP | DS06 | Rg05 | Rg1 | EM | DS09 | DS03 | HM | LV | Bro217 | GeoMean
0.1% | 29.6117 | 3.6897 | 3.4987 | 1.6516 | 2.9781 | 0.89892 | 7.4504 | 0.94592 | 1 | 1.0557 | 4.8159 | 1.4258 | 1.3935 | 1 | 1.4012 | 1 | 1.995 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1.8641
1% | 54.6129 | 4.2353 | 3.9557 | 5.0214 | 3.3017 | 0.90244 | 7.9545 | 1 | 1 | 5.3745 | 4.8242 | 1.7768 | 1.7483 | 0.74804 | 1.373 | 1 | 1.9978 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 2.1724
29
54
7.5
8
1.9
2.2
If the AP size is smaller, more applications will have speedups.
Notes: We also evaluate our results using a smaller AP, in which more applications have speedup.

## Slide 91: AES implementation on GPU
Symmetric Encryption with 128-bit key and 10 rounds.
S-box implementation involves table lookups.
[Jiang/Fei/Kaeli, HPCA’16] demonstrated that the last round is vulnerable.

## Slide 92: Topological-order-based Partition
Notes: To

## Slide 93: How to Predict Hot/Cold?
Training
Testing
% from Training | 100% | 20% | 2% | 0.2%
Accuracy | 97% | 93% | 90% | 87%
% from Input | 50% | 10% | 1% | 0.1%
Use a small profiling input to predict the hot/cold states
Notes: First, we discuss how do we predict hot and cold states.
We use a simple profiling input to predict the hot and cold states.
To evaluate how a representative profiling input can predict the real situation in the execution, we evaluate the prediction in this methodology.
Each application has an 1MB input.
We split the input to two disjoint equal parts, which are training input and testing input.
We select different sizes of training input. We evaluate the accuracy of prediction by using different sizes of training input.
In our finial results, we use 1% and 0.1% of input.