## Slide 1: ACACES 2018 Summer School GPU Architectures: Basic to Advanced Concepts
Adwait Jog, Assistant Professor
College of William & Mary (http://adwaitjog.github.io/)

## Slide 2: William & Mary
Second oldest-institution of higher education in the USA
Located in Williamsburg, VA, USA. Recently hosted ASPLOS conference – one of the top venues for computer architecture research.
I am affiliated with Computer Science Department
  Graduate Program (~65-70 Ph.D. students)
  25 Faculty Members
Many graduated Ph.D. students have successfully established careers in academia & industry.

## Slide 3
Brief Introduction
Adwait Jog
(Assistant Professor)
  Interested in developing high-performance, energy-efficient and scalable systems that are low cost, reliable, and secure.
  Special focus on GPU architectures and accelerators.
  I lead Insight Computer Architecture
  Lab at College of William and Mary
  (http://insight-archlab.github.io/)
  Our lab is funded by
  US National Science Foundation (NSF) and
  always looking to hire bright students at all levels.

## Slide 4: Journey of CMPs: Scaling and Heterogeneity Trends
Intel 4004,
1971
1 core,
no cache
23K transistors
Intel 8088,
1978
1 core,
no cache
29K transistors
Intel Pentium 4,
2000
1 core
256 KB L2 cache
42M transistors
Intel Sandy Bridge,
2011
6 cores
15 MB L3 cache
2270M transistors
What’s now?

## Slide 5: Intel Core i7-6700K Processor, 2016 (Skylake)
1.7 billion transistors, 14 nm process, die size 122 mm2
Notes: image source probably Intel, available at many places

## Slide 6: Intel Quad Core GT2, 2017 (Kaby Lake)
14 nm process, die size 126 mm2

## Slide 7: I) Graphics Portion on CMPs is Growing
Intel Coffee Lake
AMD Raven Ridge

## Slide 8: II) Graphics Cards are Becoming More Powerful
GTX 980
(Maxwell)
2048
CUDA
Cores
(224
GB/sec)
GP 100
(Pascal)
3584
CUDA
Cores
(720
GB/sec)
GV 100
(Volta)
5120
CUDA
Cores
(900
GB/sec)
GTX 680
(Kepler)
1536
CUDA
Cores
(192
GB/sec)
GTX 275
(Tesla)
240
CUDA
Cores
(127
GB/sec)
GTX 480
(Fermi)
448
CUDA
Cores
(139
GB/sec)
2008 2010 2012 2014 2016 2018
Notes: As we know GPU are scaling both in terms of number of CUDA cores as well peak DRAM
Bandwidth. For example, the latest NVIDIA GPU GTX 980 has more than 2000 cores.
Given such powerful GPUs, the question is -- Are we “still” using them efficiently?

## Slide 9: III) GPUs are Becoming Ubiquitous

## Slide 10: IVa) GPUs are Becoming More Useful
ENABLING
Scientific COMPUTING
&
BREAKTHROUGHS
BACKEND OF “Google”
&
many others
HELPS UNDERSTAND UNIVERSE

## Slide 11: IVb) GPUs are Becoming More Useful
Astronomy
Medical
Imaging
Audio
Processing
Machine
Learning
Physics
Simulation
Games
Image Processing
Financial Computing
Genomics
Data-Level Parallelism
Large
Data Sets

## Slide 12: IVc) GPUs are Becoming More Useful
Deep Learning and Artificial Intelligence
Credit: NVIDIA AI
There are several performance and energy bottlenecks in GPU-based systems that need to be addressed via software- and/or hardware-based solutions.
There are emerging security-concerns also that need to be addressed via software- and/or hardware-based solutions.

## Slide 13: Course Outline
Lectures 1 and 2: Basics Concepts
  Basics of GPU Programming
  Basics of GPU Architecture
Lecture 3: GPU Performance Bottlenecks
  Memory Bottlenecks
  Compute Bottlenecks
  Possible Software and Hardware Solutions
Lecture 4: GPU Security Concerns
  Timing channels
  Possible Software and Hardware Solutions

## Slide 14: Lecture Material
Available at my webpage (http://adwaitjog.github.io/). Navigate to the teaching tab
Direct link: http://adwaitjog.github.io/teach/acaces2018.html
Material will updated over the week – so keep checking the website periodically
The lecture material is currently preliminary and small changes are likely. Follow the class lectures!

## Slide 15: Course Objectives
By the end of this (short) course, I hope you can appreciate
  the benefits of GPUs
  the architectural differences between CPU and GPU
  the key research challenges in the context of GPUs
  some of the existing research directions
I encourage questions during/after the class
  Ample time for discussions during the week
  Find me during breaks or email me

## Slide 16: Background
My assumption is that students have some background on basic computer organization and design.
Question 1: How many of you have taken undergraduate-level course on computer architecture?
Question 2: How many of you have taken graduate-level course on computer architecture?
Question 3: How many of you have taken a GPU course before?

## Slide 17: Reading Material (Books & Docs)
D. Kirk and W. Hwu, “Programming Massively Parallel Processors – A Hands-on Approach, 3rd Edition”
Patterson and Hennesy, Computer Organization and Design, 5th Edition, Appendix C-2 on GPUs
Aamodt, Fung, Rogers, “General-Purpose Graphics Processing Architectures” – Morgan & Claypool Publishers, 1st Edition (New book!)
Nvidia CUDA C Programming Guide
  https://docs.nvidia.com/cuda/cuda-c-programming-guide/

## Slide 18: Course Outline
Lectures 1 and 2: Basics Concepts
  Basics of GPU Programming and Architecture
Lecture 3: GPU Performance Bottlenecks
  Memory Bottlenecks
  Compute Bottlenecks
  Possible Software and Hardware Solutions
Lecture 4: GPU Security Concerns
  Timing channels
  Possible Software and Hardware Solutions

## Slide 19: GPU vs. CPU
GPU Memory
Cache
ALU
Control
ALU
ALU
ALU
CPU Memory
CPU
GPU

## Slide 20: Why use a GPU for computing?
GPU uses larger fraction of silicon for computation than CPU.
At peak performance GPU uses order of magnitude less energy per operation than CPU.
CPU
2nJ/op
GPU
200pJ/op
Rewrite Application
Order of Magnitude More Energy Efficient
However….
Application must perform well

## Slide 21: How Acceleration Works
Fewer Cores
Optimized for Latency
Great for Sequential Code
Large Number of Cores
Optimized for Throughput
Great for
Parallel Code
Application Code
Sequential Code
Parallel Code
Sequential Code
Many Top 20 supercomputers
in the green500 list employ accelerators.
Accelerator
(e.g., GPU)
Notes: Do not use the word “offload”

## Slide 22: Fastest Super Computer* -- SUMMIT @ Oak Ridge
Multiple Volta GPUs
NVLink
HBM + DDR4
https://www.olcf.ornl.gov/olcf-resources/compute-systems/summit/
* As of June 2018

## Slide 23
  CPU (Host) GPU (Device)
How is this system programmed (today)?
CPU Memory
GPU Memory

## Slide 24
GPU Programming Model
CPU
spawn
done
GPU
CPU
Time
CPU
spawn
GPU
CPU (host) “off-load” parallel kernels to GPU (device)
  Transfer data to GPU memory
  GPU spawns threads
  Need to transfer result data back to CPU main memory

## Slide 25: CUDA Execution Model
Application Code
  Serial parts (C code) in CPU (host)
  Parallel parts (Kernel code) in GPU (device)
Serial Code (host)‏
. . .
. . .
Parallel Kernel (device)‏
KernelA<<< nBlk, nTid >>>(args);
Serial Code (host)‏
Parallel Kernel (device)‏
KernelB<<< nBlk, nTid >>>(args);
Serial Code (host)‏
Application

## Slide 26
Block 1
Block 2
Kernel 1
Kernel
Application
Kernel 2
Kernel 3
Block 3
Warp 1
CTA
Warp 2
Warp 3
Warp 4
Threads
GPU as SIMD machine
At a high-level, multiple threads work on same code (instructions) but different data
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1

## Slide 27: Kernel: Arrays of Parallel Threads
A CUDA kernel is executed by a grid of threads
  All threads in a grid run the same kernel code (Single Program Multiple Data)‏
  Each thread has indexes that it uses to compute memory addresses and make control decisions
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
0
1
2
254
255
Thread Block 0
…
1
2
254
255
Thread Block 1
0
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
1
2
254
255
Thread Block N-1
0
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
…
…
…

## Slide 28: Kernel, Blocks, Threads

## Slide 29: Vector Addition Example
A[0]
vector A
vector B
vector C
A[1]
A[2]
A[N-1]
B[0]
B[1]
B[2]
…
…
B[N-1]
C[0]
C[1]
C[2]
C[N-1]
…
+
+
+
+

## Slide 30: Vector Addition – Traditional C Code
// Compute vector sum C = A + B
void vecAdd(float *h_A, float *h_B, float *h_C, int n)
{
int i;
for (i = 0; i<n; i++) h_C[i] = h_A[i] + h_B[i];
}
int main()
{
// Memory allocation for h_A, h_B, and h_C
// I/O to read h_A and h_B, N elements
…
vecAdd(h_A, h_B, h_C, N);
}

## Slide 31: vecAdd CUDA Host Code
#include <cuda.h>
void vecAdd(float *h_A, float *h_B, float *h_C, int n)‏
{
int size = n* sizeof(float);
float *d_A, *d_B, *d_C;
// Part 1
// Allocate device memory for A, B, and C
// copy A and B to GPU (device) memory
// Part 2
// Kernel launch code – the device performs the vector addition
// Part 3
// copy C from the device memory
// Free device vectors
}

## Slide 32: Vector Addition (Host Side)
void vecAdd(float *h_A, float *h_B, float *h_C, int n)
{
int size = n * sizeof(float); float *d_A, *d_B, *d_C;
cudaMalloc((void **) &d_A, size);
cudaMalloc((void **) &d_B, size);
cudaMalloc((void **) &d_C, size);
cudaMemcpy(d_A, h_A, size, cudaMemcpyHostToDevice);
cudaMemcpy(d_B, h_B, size, cudaMemcpyHostToDevice);
// Kernel invocation code – to be shown later
cudaMemcpy(h_C, d_C, size, cudaMemcpyDeviceToHost);
// do processing of results
cudaFree(d_A); cudaFree(d_B); cudaFree (d_C);
}

## Slide 33: Kernel Invocation code (Host Side)
void vecAdd(float *h_A, float *h_B, float *h_C, int n)
{
….. Preparation code (See previous slide)
int blockSize, gridSize;
// Number of threads in each thread block
blockSize = 1024;
// Number of thread blocks in grid
gridSize = (int)ceil((float)n/blockSize);
// Execute the kernel
vecAdd<<<gridSize, blockSize>>>(d_A, d_B, d_C, n);
… Post-processing (See previous slide)
}

## Slide 34: Kernel Code (Device Side)
__global__ void vecAdd(double *a, double *b, double *c, int n)
{
// Get our global thread ID
int id = blockIdx.x*blockDim.x+threadIdx.x;
// Make sure we do not go out of bounds
if (id < n)
c[id] = a[id] + b[id];
}
Same code is run by several threads

## Slide 35: Important CUDA Syntax Extensions
Declaration specifiers
  __global__ void foo(...); // kernel entry point (runs on GPU)
Syntax for kernel launch
  foo<<<500, 128>>>(...); // 500 thread blocks, 128 threads each
Built in variables for thread identification
  dim3 threadIdx; dim3 blockIdx; dim3 blockDim;

## Slide 36: Example: Original C Code
void saxpy_serial(int n, float a, float *x, float *y)
{
for (int i = 0; i < n; ++i)
y[i] = a*x[i] + y[i];
}
int main() {
// omitted: allocate and initialize memory
saxpy_serial(n, 2.0, x, y); // Invoke serial SAXPY kernel
// omitted: using result
}
Notes: saxpy = single precision ax + y

## Slide 37: CUDA Code
__global__ void saxpy(int n, float a, float *x, float *y) {
int i = blockIdx.x*blockDim.x + threadIdx.x;
if(i<n) y[i]=a*x[i]+y[i];
}
int main() {
// omitted: allocate and initialize memory
int nblocks = (n + 255) / 256;
cudaMalloc((void**) &d_x, n);
cudaMalloc((void**) &d_y, n);
cudaMemcpy(d_x,h_x,n*sizeof(float),cudaMemcpyHostToDevice);
cudaMemcpy(d_y,h_y,n*sizeof(float),cudaMemcpyHostToDevice);
saxpy<<<nblocks, 256>>>(n, 2.0, d_x, d_y);
cudaMemcpy(h_y,d_y,n*sizeof(float),cudaMemcpyDeviceToHost);
// omitted: using result
}
Runs on GPU
Notes: saxpy = single precision ax + y

## Slide 38: Code to Hardware Mapping

## Slide 39: Code to Hardware Mapping: Transparent Scalability
Each block can execute in any order relative to others.
GPU Hardware is free to assign blocks to any processor at any time
  A kernel scales to any number of parallel processors.
GPU-2 (Device - 2)
P
P
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Kernel
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
GPU-1 (Device - 1)
P
P
P
P
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Case-1
Case-2

## Slide 40: Streaming Multi-Processor (SM)
Scratchpad
Control
SM
GPU-1 (Device - 1)
SM
SM
SM
SM
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Register File
Threads are assigned to SM in block granularity
SM maintains thread/block idx #s
SM manages/schedules thread execution
Multiple blocks can be allocated to the SM
  Based on the amount of resources (shared memory, register file etc.)

## Slide 41: GPU Execution Model
Blocks assigned to each SM are scheduled on the associated SIMD hardware (i.e., on the Processing Elements (PEs)).
SM bundles threads (from various blocks) into warps (wavefronts) and runs them in lockstep on across PEs.
An NVIDIA warp groups 32 consecutive threads together (AMD wave-fronts group 64 threads together)
Warps are:
  Scheduling units in SM
  Scheduled in multiplexed and pipelined manner on the SM
Notes: MIMD = multiple-instruction, multiple-data

## Slide 42: Warp Example
If 3 blocks are assigned to an SM and each block has 256 threads, how many warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 0 Warps
Block 1 Warps
…
t0 t1 t2 … t31
…
Block 2 Warps
Register File
Scratchpad

## Slide 43: Tolerating Long Latencies
Execution in an SM
W1
W2
W3
Computation
Waiting for Data from GPU Memory
GPU attempts to hide long memory latency with computation from
other warps
How SMs are able to context switch between warps so quickly?

## Slide 44: Summary
Spawns more threads than GPU can run (some may wait)
Organize threads into “blocks” (up to 1024 threads per block)
Motivation: Write parallel software once and run on future hardware
Warps associated with blocks can help in tolerating long latencies.
GPUs support large register files (for fast context switching) and high bandwidth memories (for providing data to large number of concurrent threads)

## Slide 45: Reading Material
D. Kirk and W. Hwu, “Programming Massively Parallel Processors – A Hands-on Approach, 3rd Edition”
Patterson and Hennesy, Computer Organization and Design, 5th Edition, Appendix C-2 on GPUs
More background material: Jog et al., OWL: Cooperative Thread Array Aware Scheduling Techniques for Improving GPGPU performance, ASPLOS’13
Nvidia CUDA C Programming Guide
  https://docs.nvidia.com/cuda/cuda-c-programming-guide/