## Slide 1: ACACES 2018 Summer School GPU Architectures: Basic to Advanced Concepts
Adwait Jog, Assistant Professor
College of William & Mary (http://adwaitjog.github.io/)
Some of the slides are borrowed from the NVIDIA Teaching Kit, Tor Aamodt’s (UBC) course on GPUs

## Slide 2: Course Outline
Lectures 1 and 2: Basics Concepts
  Basics of GPU Programming
  Basics of GPU Architecture
Lecture 3: GPU Performance Bottlenecks
  Memory Bottlenecks
  Compute Bottlenecks
  Possible Software and Hardware Solutions
Lecture 4: GPU Security Concerns
  Timing channels
  Possible Software and Hardware Solutions

## Slide 3: Era of Heterogeneous Architectures
Intel Coffee Lake and
Kaby Lake
AMD Raven Ridge

## Slide 4: Discrete GPUs

## Slide 5: Discrete GPUs + Intel Processors

## Slide 6: Security Concerns
GPUs may be accelerating applications that are using user-sensitive data (e.g., genomics, financial)
GPUs may be accelerating cryptographic applications (e.g., AES, RSA etc.) and authentication algorithms on-behalf of CPUs
Given the popularity of GPUs, it is imperative to keep GPUs secure against a variety of side-channel attacks and other security vulnerabilities.

## Slide 7: Security Attacks
User’s web activity on GPU can be tracked by the malicious attacker who is co-located on the same card [Oakland’14]
AES private keys can be recovered by correlation timing attacks [HPCA’16]
Accelerating attacks via GPUs [Oakland’18]
  Glitch: Accelerating row hammer attacks

## Slide 8: Correlation Timing Attacks
Plaintexts | Ciphertexts | Time duration
Plaintext # 1
time1
timestart
- timestop = time1
Plaintext # 2
time2
Plaintext # 3
time3
…
…
Outside Attacker
Server@GPU
Ciphertext # 1
Ciphertext # 2
Ciphertext # 3
…
K1 , K2 , … ,
Ki
, …
Key guesses
Correct Key
Correct Key??
Notes: This should be a general timing attack description

## Slide 9: Memory Access Coalescing in GPUs
Computing Unit
Wavefront pool
Wavefront
Thread # 1
Thread # 32
. . .
Scheduler
LD/ST Unit
Global Memory
Coalescing Unit

## Slide 10: Memory Access Coalescing in GPUs
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x00
0x04
0x07
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Wavefront
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 1
Block Address # 2

## Slide 11: Memory Access Coalescing in GPUs
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
0x00
0x04
0x07
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Wavefront
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 2

## Slide 12: AES implementation on GPU
Symmetric Encryption with 128-bit key and 10 rounds.
S-box implementation involves table lookups.
[Jiang/Fei/Kaeli, HPCA’16] demonstrated that the last round is vulnerable.

## Slide 13: Last Round of AES on GPU

## Slide 14: Last Round of AES on GPU
LINE # 1
LINE # 2
LINE # 32
…
…
ti1
ti2
ti32
.
.
.
Input text
to Last Round
…
…
.
.
.
Thread # 1
Thread # 2
.
.
.
Thread # 32
.
.
.
T4[ti2]
T4[ti1]
T4[ti32]
Request # 1
Request # 2
.
.
.
Request # 32
Coalescing
Unit
.
.
.
⊕kj
⊕kj
⊕kj
Replies # 1
Replies # 2
.
.
.
Replies # 32
cj1
cj2
cj32
.
.
.
Ciphertext

## Slide 15: Correlation Timing Attack on GPU
Goal of the attack: Recover the AES Key (byte-by-byte)
Last Round of AES is vulnerable
Last Round is invertible
Memory access
of thread tid
How an attacker can calculate the number of coalesced accesses?
Notes: After the goal, Attack model – using figure slide 2. What is available to the attacker – ciphertext, execution time and AES Tables.

## Slide 16: Attacker calculates the # of coalesced accesses
…
…
cj1
cj2
cj32
.
.
.
Ciphertext
.
.
.
⊕kjm
⊕kjm
⊕kjm
.
.
.
.
.
.
T4-1[cj2⊕kjm]
T4-1[cj1⊕kjm]
T4-1[cj32⊕kjm]
ti1,m
ti2,m
ti32,m
.
.
.
Guessed Table
Lookup Indices
.
.
.
.
.
.
Coalesced Accesses
(Ajm,n)
Correct value of key byte?

## Slide 17: Coalesced Accesses and Execution Time
Associate the number of coalesced accesses with execution time
Notes: Say on our set-up

## Slide 18: Finding the Correct Key Value
Attacker encrypts ‘N’ number of plaintexts over server
  Records Ciphertext and Execution time
Aj0,1, Aj0,2, . . . . , Aj0,N
E1,E2,...,EN
Key Guess 0
Key Guess 1
Key
Guess 255
Corrj0
Corrj1
Corrj255
Key
Guess α
Corrjα
Maximum Correlation
Aj1,1, Aj1,2, . . . . , Aj1,N
Ajα,1, Ajα,2, . . . . , Ajα,N
Aj255,1, Aj255,2, . . . . ,Aj255,N
.
.
.
.
.
.
.
.
.
.
.
.
Recorded
Execution Time
Correct
Key Byte
# of Coalesced Accesses
Correlations
Notes: Eliminate the slide transition

## Slide 19: Simulating Timing Attack on our Set-up
Correct guess
Incorrect guesses
Why is Correlation Timing Attack possible?
The baseline attack leverages the deterministic nature of the coalescing mechanism
AES key value affects the coalesced accesses
# coalesced accesses affects the execution time
How to mitigate Correlation Timing Attacks on GPU?
Answer: By making it harder for the attacker to correctly calculate the number of coalesced accesses
Notes: TODO: Coalescing good for performance and bad for security

## Slide 20: Naïve Solution
Disable coalescing altogether?
  Correlation drops to ~0
  Correct key byte is indistinguishable
Up to 178% performance degradation
  Degradation increases with plaintext size
Correct guess
Naïve solution is Good for Security, Bad for Performance
Offers no tradeoff
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps (or subwavefronts)
  Fixed sizes of subwarp (or subwavefronts)
  Deterministic mapping of the thread elements to subwarps (or subwavefronts)
RCoal to mitigate the correlation timing
attacks

## Slide 21: RCoal: Fixed Sized Subwarp (FSS)
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
DEFAULT: number of subwarps = 1
0x00
sid = 0
0x04
0x07
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
FSS: number of subwarps = 2
0x00
sid = 0
0x04
0x07
sid = 1
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Notes: Fixed Size Subwarp eliminates the fixed number of subwarps based determinism.

## Slide 22: FSS Security against Baseline Attack
Correlation between the number of coalesced accesses and the execution time drops
Correct key byte is harder to find
Improved security

## Slide 23: FSS Performance
Memory accesses increase with number of subwarps
Execution time increases with number of subwarps
Performance degrades as number of subwarp increase
Can attacker still recover the AES key?
Notes: Better transition going into FSS attack

## Slide 24: FSS against FSS attack
Attacker can figure out the number of subwarps
Notes: Why FSS attack?

## Slide 25: FSS against FSS attack
Attacker can figure out the number of subwarps
Attacker can calculate per subwarp accesses
Correct guess

## Slide 26: FSS against FSS attack
Attack possible when the attacker can figure out number of subwarps!
  Coalescing still deterministic
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 27: RCoal: Random Sized Subwarp (RSS)
Size distribution
Normal Distribution
Skewed Distribution
Mean of the distribution is same as FSS
Security and performance similar to FSS
We select RSS with Skewed Distribution
Mean of the distribution is different than FSS
Large subwarp offers better coalescing
Improved security compared to FSS
Improved performance compared to FSS


RCoal to mitigate the correlation timing
attacks
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 28: RCoal: Random-Threaded Subwarp (RTS)
FSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 0
0x06
sid = 1
0x07
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
FSS+RTS: number of subwarps = 2
0x00
0x01
0x06
0x07
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x04
0x05
0x06
0x07
sid = 0
sid = 0
sid = 1
sid = 1

## Slide 29: RCoal: Random-Threaded Subwarp (RTS)
RSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 1
0x06
0x08
tid = 0
tid = 1
tid = 2
tid = 3
RSS+RTS: number of subwarps = 2
0x00
sid = 1
0x01
0x06
sid = 0
0x08
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B

## Slide 30: Evaluation Set-up
AES-128
Plaintext with 32 lines
GPGPU-SIM
  15 SMs, 32 threads/warp, one subwarp per coalescing unit (base case)
  GDDR5 Memory with 6 MCs, 16 DRAM-banks, 4 bank-groups/MC
Enhanced Attack Algorithms
  Corresponding Attacks

## Slide 31: Performance/Security Trade-off
Chart: Number of Subwarps
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0
FSS | 0.99846 | 0.99941 | 0.99935 | 0.99771 | 0.94154 | 0
FSS+RTP | 0.99846 | 0.42426 | 0.2569 | 0.080777 | 0.04366 | 0
RSS | 0.99846 | 0.2467 | 0.15489 | 0.13513 | 0.14823 | 0
RSS+RTP | 0.99846 | 0.15216 | 0.095578 | 0.10696 | 0.065268 | 0
Chart: Number of Subwarps
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0
FSS | 1 | 1.0822 | 1.1525 | 1.2189 | 1.2788 | 1.3801
FSS+RTS | 1 | 1.082 | 1.1527 | 1.2198 | 1.2787 | 1.3801
RSS | 1 | 1.0538 | 1.104 | 1.1534 | 1.2455 | 1.3801
RSS+RTS | 1 | 1.0544 | 1.1013 | 1.1547 | 1.2455 | 1.38
Security
(Lower the better)
Execution Time
(Lower the better)
Offers Security/Performance Trade-off
Notes: Mention Rcoal in a BOX

## Slide 32: Conclusions
We discussed RCoal, a set of three novel defense mechanisms
  To mitigate the correlation timing attacks
  Randomizes the memory access coalescing
  Scales with the plaintext size (analysis in paper)
  Theoretical analysis in the paper
RCoal offers a trade-off between security and performance and improves security at a modest performance loss.
Notes: Try to reduce background and introduce rcoal_score

## Slide 33: Food for thought
Improving security at lower performance cost
  Can we randomize logic at other parts of the memory hierarchy?
    GPU Cache Management
    GPU Bandwidth Management (e.g., MSHRs)
    GPU Prefetching and Memory Scheduling
  Can we leverage software-driven hints?
    Only randomize when “security-critical” sections of the code are executing
    How do we identify “security-critical” sections? If yes, can we automate the process?

## Slide 34: References
RCoal: Mitigating GPU Timing Attack via Subwarp-based Randomized Coalescing Techniques, HPCA’18
A Complete Key Recovery Timing Attack on a GPU, HPCA’16
Grand Pwning Unit: Accelerating Microarchitectural Attacks with the GPU, Oakland’18